## Slide 1
An implementing guide
to DRA audio decoder
in a DTMB receiver
Digital Rise Co.,Ltd, Guangdong, China
(National Engineering Laboratory for Audio Technology)
2011.10.24
Notes: <number>
26/7/28

## Slide 2: Contents
DTMB receiver
DRA in a DTMB receiver
Technical details of the NP
Schedule
Notes: <number>
26/7/28

## Slide 3
DTMB receiver
DRA in a DTMB receiver
Technical details of the NP
Schedule
Notes: <number>
26/7/28

## Slide 4: DTMB receiver standard (1)
GB/T 26686-2011 DTMB receiver standard, China
  Name: General specification for terrestrial digital television receivers
  Issued date: 16th June 2011
  Effective date: 1st November 2011
IEC 100/1855/NP “Digital Terrestrial Television Receivers for the DTMB system”

## Slide 5: A few main modules of a DTMB receiver
DTMB
Demoduating
Channel decoding
Demux
Video decoder
Audio decoder

## Slide 6: The Channel processing of a DTMB receiver
Digital Terrestrial/Television Multimedia Broadcasting (DTMB) standard:
  GB 20600-2006: DTV-terrestrial transmitting China National Standard
  The full tile : “Framing structure, channel coding and modulation for digital television terrestrial broadcasting system”.
DTMB
Demoduating
Channel decoding
Demux
Video decoder
Audio decoder

## Slide 7: Video decoding of a DTMB receiver
Video decoding
  ISO/IEC 13818-2(MPEG-2)
  GB/T 20090.2-2006 (Chinese standard) AVS Video decoding
  specified frame rate as 25Hz, 4:3 and 16:9 ratio
DTMB
Demoduating
Channel decoding
Demux
Video decoder
Audio decoder

## Slide 8: Audio decoding of a DTMB receiver
Audio decoding
  ISO/IEC 11172-3 MPEG-1 Layer II
  GB/T22726-2008, China: DRA audio decoding
  ETSI TS 102366 (AC3) or other digital audio stream
DTMB
Demoduating
Channel decoding
Demux
Video decoder
Audio decoder

## Slide 9
DTMB receiver
DRA in a DTMB receiver
Technical details of the NP
Schedule
Notes: <number>
26/7/28

## Slide 10: DRA – Chinese audio decoding standard
  DRA (Digital Rise Audio) standard
  Name：《Specification for Multichannel
  Digital Audio Coding Technology 》
  Number ： GB/T 22726-2008
  Issued date： Dec 22, 2008
  Used in the fields of: Blu-ray Disc, DTMB,
  CMMB, and etc.
  Published in Chinese

## Slide 11: Other DRA–related international standards
  IEC 61937-12 2010: Digital audio - Interface for non-linear PCM encoded audio bitstreams applying IEC 60958 - Part 12: Non-linear PCM bitstreams according to the DRA formats, by TC100/TA4
  CEA and HDMI 2010: CEA 861.1 “Audio Format Extensions”
  IETF 2009: “RTP Payload Format for DRA Audio”
  IANA 2009: “MIME media type name & MIME subtype name for DRA”
  SMPTE 2008： “DRA Elementary Streams in the MPEG-2 Multiplex”
  MP4 2008： “ MP4 File Format for DRA Audio ”
  DRA is an optional audio decoding technology in BD-ROM standard
    Included in “System Description Blue-ray Disc Read-Only Format, Part3: Audio Visual Basic Specifications V2.3” (March, 2009)
No guide to DRA decoder implementation in above standards

## Slide 12: DRA in a DTMB receiver
DRA is a mandatory audio decoder in DTMB receiver standard
  It is described in section 5.5.2.1.1 of DTMB receiver standard in Chinese
No official English version to define how to decode DRA data in a DTMB receiver
“A guide for implementing DRA decoder in a DTMB receiver”
can firstly be standardized by IEC TC100/TA1
as IEC 100/1855/NP “Digital Terrestrial Television Receivers for the DTMB system” part 2

## Slide 13
DTMB receiver
DRA in a DTMB receiver
Technical details of the NP
Schedule
Notes: <number>
26/7/28

## Slide 14: IEC 100/1855/NP --- part 2
Title: A guide for implementing DRA decoder in a
DTMB receiver
Contents
  Overview of a DRA decoder
  Describe the syntax structure of DRA data stream
  Explain the implementation steps of DRA decoding modules
  Limitations for DRA decoder in DTMB receiver

## Slide 15: DRA Decoder (1) overview

## Slide 16: DRA Decoder (2) frame structure

## Slide 17: DRA Decoder (2-1)
Decoder Components | Function
Demultiplexer | Decode each code from bit stream packet. Because the Huffman code is the prefix code, the decoding and demultiplexing are processed on the same step.
Code Book Selector | Decode each Huffman code book and its application range from bit stream for decoding quantization index.
Quantization Index Decoder | Decode quantization index from bit stream.
The Number of quantization unit Reconstructor | Reconstruct the number of quantization units for each transient cluster according to code book application range.
Dequantizer | Decode quantization step sizes of all the quantization units from bit stream, and reconstruct the subband samples according to quantization index.

## Slide 18: DRA Decoder (2-2)
Decoder Components | Function
Optional Joint Intensity Decoder | Reconstruct the subband samples of joint channel from the subband samples in source channel by using joint intensity scale factor.
Optional Sum/Difference Decoder | Reconstruct the subband samples of left/right channel from the subband samples in sum/difference channel.
De-interleaving | De-interleaving is carried out, when there is transient in the frame.
Short/Brief windows function sequence Reconstructor | Reconstruct the short/brief window function sequence for the transient frame by the transient location and the MDCT perfect reconstruction condition.
Variable Resolution Synthesis Filter Bank | Reconstruct the PCM audio samples from subband samples.

## Slide 19: DRA Limitations for DTMB receiver
sampling rate | 8~192kHz
bit rate | 32~9612kpbs
sampling precision | 24 bits
channel numbers | 64.3 —— normal channels: 64, low frequency channels (LFE):3
Original Specs of DRA audio coding technology
Limited Specs of DRA
sampling rate | Shall support 48 kHz, 44.1 kHz, and 32 kHz, others are optional
bit rate | ≥ 128kpbs
sampling precision | 24 bits
channel numbers | Stereo, 5.1 surround and more

## Slide 20
DTMB receiver
DRA in a DTMB receiver
Technical details of the NP
Schedule
Notes: <number>
26/7/28

## Slide 21: Time plan
CN-NC evaluate the NP before 2012
if accepted
NP document Mar. 2012
Date of Circulation (NP) Apr. 2012
if accepted
The first CD Oct. 2012
IS 2013

## Slide 22
Thanks！
NELA：www.nela.org.cn