## Slide 1: UHD Terminology Analysis & Suggestions
IEC TC100
CHINA NC

## Slide 2: Background
Purpose :
-. to analysis the necessity of the “UHD Terminology” project
References :
-. IEC 60050：International Electro-technical Vocabulary
-. IEC TC110 OLED -1-2 FDIS : Terminology and letter symbols
-. IEC 61747-1-2： Generic-Terminology and Letter symbols
（Need to be checked）

## Slide 3: Terminology Analysis & Suggestions
Terms | TC100 UHD Terminology (Working-draft) | IEC 60050 | TC110 OLED-1-2 FDIS | Comments
Response time | Process time that television (monitor) pixel from dark to light, express as “rise time” and “fall time” | 431-02-12：the time from a sudden change of a control quantity until the corresponding change of an output quantity has reached a specified fraction of its final value | generic term for "turn-on time"and "turn-off time" | the main contents are similar : "turn-on time" is the same meaning with "rise time",and "turn-off time" is the same meaning with "fall time"

## Slide 4: Terminology Analysis & Suggestions
Terms | TC100 UHD Terminology (Working-draft) | IEC 60050 | TC110 OLED-1-2 FDIS | Comments
Rise time | Time interval in which luminance changes from 10 % to 90 % after switching on | 521-05-22：time interval between the instants at which the magnitude of the pulse at the output terminals reaches specified lower and upper limits respectively when the semiconductor device is being switched from its non-conducting to its conducting state 531-44-14：the time required for the photoelectric current to rise from a stated low percentage to a stated higher percentage of the maximum value when a steady state of radiation is instantaneously applied | time interval at which luminance changes from 10% to 90% after swithching organic light emitting diode display driving voltage from OFF state to ON state. | the main contents are similar : the key is "luminance changes from 10% to 90%"

## Slide 5: Terminology Analysis & Suggestions
Terms | TC100 UHD Terminology (Working-draft) | IEC 60050 | TC110 OLED-1-2 FDIS | Comments
Fall time | Time interval in which luminance change from 90 % to 10 % after switching off | 521-05-24：time interval between the instants at which the magnitude of the pulse at the output terminals reaches specified upper and lower limits respectively when a semiconductor device is being switched from its conducting to its non-conducting state 531-44-15：the time required for the photoelectric current to fall from a stated high percentage to a stated lower percentage of the maximum value when a steady state of radiation is instantaneously removed | time interval between the sintants at which the luminance is 90% and 10% of between the luminance of the ON and OFF states. | the main contents are similar : the key is "luminance changes from 90% to10%"

## Slide 6: Terminology Analysis & Suggestions
Terms | TC100 UHD Terminology (Working-draft) | IEC 60050 | TC110 OLED-1-2 FDIS | Comments
Residual image | Phenomenon that still picture keep on screen with no input after inputting a still signal for long time | - | general term that refers to a burned-in image or a permanent image caused by long time static operation. | the main contents are similar : "still picture" is the same meaning with "permanent picture"

## Slide 7: Terminology Analysis & Suggestions
Terms | TC100 UHD Terminology (Working-draft) | IEC 60050 | TC110 OLED-1-2 FDIS | Comments
Colour gamut area | Ratio of RGB triangle gamut area or all colours polygon gamut area and the spectral colour gamut as defined in CIE 1976 (u’,v’) space | - | range of colors that can be reproduced by an organic light emitting diode display panel. | the main contents are similar : "range of colors" is the same meaning with "Ratio of RGB triangle gamut"

## Slide 8: Terminology Analysis & Suggestions
Conclusion:
-. We found some terms in IEC TC100 UHD Terminology already has definition in other IEC standards, So lack of necessity of establishing this standard at this stage.